## Slide 1: Mesh Walkie Talkie Research
ECEN/CSCE 403 Capstone
Jaiah, Ryan, Junsu, Cole

## Slide 2: Subsystem Split
Power System - Junsu
  Be able to power multiple systems
  Low power, transmission, and shut-down power systems
  Rechargeable Li Battery (1.8 - 3.8 MCU supply Voltage)
Audio System - Ryan
  Audio sampling/audio compression
  Push-to-talk
  ADC/DAC conversions
Mesh/RF system - Cole/Jaiah
  Mesh algorithm/software (challenge)
  Gateway Node system
MCU software/other hardware system - Team (next semester)
  All other MCU software
  Launchpad hardware integration with other components
  Case Hardware/display hardware/push-to-talk hardware etc.

## Slide 3: Mesh System
Zigbee
Wi-SUN*
Pros | Cons
Well established, abundant support | 2.4 GHz band (congestion, interference heavy)?
Higher data rate for increased audio quality | Larger power consumption
Low latency | 
Pros | Cons
Longer Range | Lower data rate, increased latency
Lower Power Consumption | Less maturity in consumer market
Less Interference | Potentially more complex, less support
In order to avoid using a main hub in our mesh topology, Wi-SUN would likely be the better option. Although abundant support exists for Zigbee, Wi-SUN is naturally designed for decentralized mesh networking, without the need for a central hub or coordinator. This allows for a more flexible deployment of walkie-talkies that can communicate directly with each other or relay messages through other nodes.

## Slide 4: Mesh System (Continued)
Wi-SUN potential restraints:
IoT Focus - Wi-SUN is optimized for IoT applications, which typically involve small, intermittent data packets (like sensor readings). Continuous audio streaming is different and may introduce protocol overhead that impacts efficiency and real-time performance.
Compression Requirements - Need to compress audio to ~200Kbps minimum while maintaining low latency
Antennas - Need antennas compatible with the sub-1 GHz band to transmit and receive signals. Included in LP?

## Slide 5: Voice Coder (Compression) Algorithms
Opus Codec
Meets all of the minimum system requirements
  Bitrates from 6 kb/s to 510 kb/s
  Sampling rates from 8 kHz (narrowband) to 48 kHz (fullband)
All of the resources are open source
Has Speech Support
Designed for low latency

## Slide 6: Power System
Rechargeable Lithium Battery
Have a low power mode available when device is not being used
Battery Management System (BMS)
  Prevent overcharging the battery or discharging the battery
  Monitor the temperature of the battery to make sure it doesn’t overheat
  Check voltages and currents
  State of Charge (SoC)
  State of Health (SoH)
Power distribution
  Make sure all loads are efficiently receiving power
  All power converters are being used efficiently
    Make sure each subsystem gets the right type of power (AC/DC) and the right values

## Slide 7: Questions
Subsystem Split - How can we develop individually to demo at the end of the semester?
Hello World - walkthrough of launchpad “hello world” c code post CCS, SDK download. (SimpleLinkSDK? SMARTRFTM Studio?)
PCB design? Are we using the launchpads in the final implementation?
Other part purchases: LCD, Analog Audio, Batteries
How many launchpads can we get? - many RF/Mesh demos require more than one launchpad

## Slide 8: Sources
https://www.uniconvergetech.in/blog/wi-sun-networks
https://opus-codec.org/